Microscopes and Lenses

Observe the slide in two different microscopes describe the image and give its magnification below

Question 1. Measure Parameters of Lens

What is the magnification =

___________________ 				___________________

Virtual Images and Real Images

A. Real Image

- Use big aperture lens

- use a distant object (i.e. look out the window) and make a real

image appear on a white screen.

Question 1. Measure Parameters of Lens

(a) What is the aperture (in cm)? A = ___________________

(b) What is the focal length (in cm)? Fo = ___________________

(c) What is the focal ratio? F/A = ___________________

Question 2: Image

Is the image erect, inverted, reversed, or both inverted and reversed? How can you tell?

B. Repeat with the candle as your light source

Question 1. Measure Parameters of Lens

(a) What is the aperture (in cm)? A = ___________________

(b) What is the focal length (in cm)? Fo = ___________________

(c) What is the focal ratio? F/A = ___________________

Telescope

The telescope is an example of the usefulness of lenses in producing images. One of the many claims to fame of Galileo Galilei is his work refining the design of a refracting optical telescope. Telescopes use combinations of lenses to produce a magnified image.

Figure 1

objectives

- Build a refracting optical telescope.

- Discuss the characteristics of real and virtual images.

Materials

| Vernier data-collection interface | Vernier Dynamics System track |
| --- | --- |
| Logger Pro or LabQuest App | Optics Expansion Kit: 10 and 20 cm double convex lenses, |

Preliminary questions

Before performing this activity, you should complete the activity called “Real Images and the Thin Lens Equation.”

1.	You’ve learned from the previous activity how to project a real image of a distant object using a double convex lens. How must you arrange an object, lens and screen to produce a real image?

2. What are the characteristics of a real image?

Procedure

Part A: Investigating Virtual Images

1.	Investigate the 15 cm double concave lens. Is it possible to project a real image as you did with the convex lenses?

2.	Look “into” the lens. Is it possible to see an image this way? This is a virtual image. How does it differ from a real image?

Part B: The Magnifying Lens

Next, we will experiment with the use of a double convex lens as a magnifying glass.

1.	Attach the screen to the track.

2.	Attach the 10 cm double convex lens to the track.

3.	Look through the double convex lens at the screen. Adjust the distance between the two until you clearly see a magnified image of the screen and its scale markers. Continue to adjust the distance to maximize the magnification of the image.

4.	Is the image produced by a magnifying glass real or virtual? How do you know?

5.	What is special about the position where the image has maximum magnification while remaining in focus?

Part C: The Telescope

Now we will make a telescope. In a previous activity, you projected the image of a distant object (the outdoors) on a screen. A telescope is a combination of this type of projection and a magnifying glass.

1.	Set up the 10 cm double convex lens and the screen in the position from Part B that yielded maximum magnification. Be sure to leave space on the opposite side of the screen for steps that follow.

2.	Use a 20 cm double convex lens to project the image of a distant object on the “back” side of the screen, as you did in “Real Image Formation.” Adjust the lens position until the projected image is in sharp focus. The final arrangement of the track should be: Window, 20 cm lens, Screen, 10 cm lens.

3.	Now remove the screen. You’ve made a telescope. The lens that was a magnifying lens is now the eyepiece, and the lens producing the real image is the objective lens.

4.	Describe the image you see when looking through the eyepiece. Is it upright or inverted? Magnified or reduced? Real or virtual? How do you know?

5.	What is special about the distance between the two lenses?

6.	Look through the lenses from the other direction. How does the image seen through the eyepiece compare?

Analysis

In a refracting optical telescope, a real image of a distant object is produced in the space between the lenses. A second lens produces a magnified virtual image. Below is a ray diagram of the two lenses, the real image, and the virtual image.

Figure 2: Ray Diagram of a Telescope

Aperture and Depth of Field

Lenses are used in a variety of everyday applications. In a camera, a real image is produced when light from a source passes through a lens and an opening, called the aperture, before striking film or a sensor. The size and shape of the aperture affects how much light strikes the film or sensor, and also affects some characteristics of the image. In this activity, you will investigate the role of the aperture in image formation.

Figure 1

objectives

- Predict and observe the effect of aperture adjustments real image formation.

- Observe the relationship between aperture and depth of field.

Materials

| Vernier data-collection interface | Vernier Dynamics System track |
| --- | --- |
| Logger Pro 3 or LabQuest App | Vernier Optics Expansion Kit: light source, aperture assembly, 20 cm double convex lens, screen |

Part A: The Half-Lens

1.	Set up the Optics Expansion Kit on the Dynamics System track with the light source at 10 cm, the 20 cm double convex lens at 40 cm, and the screen at 110 cm. (See Figure 1.)

2.	Turn the disc on the light source to the numeral “4.” Adjust the position of the components until a real image is projected in sharp focus on the screen.

3.	Prepare the aperture assembly by turning it to the largest opening.

4.	Place the aperture assembly on the track, immediately adjacent to the lens at around 40 cm. (Either side is OK.) Describe the image you see on the screen.

5.	The aperture has a setting that covers half the lens vertically, so the opening is in the shape of a “D.” Predict how the appearance of the image will change when half the lens is covered.

6.	Adjust the aperture assembly to the D-shaped opening. What do you observe? How does that compare with your prediction?

7.	Predict what will happen to the image as the round aperture is made smaller and smaller. Try it. What do you observe? How does that compare to your prediction? Why might this be happening?

Part B: Aperture and depth of field

1.	Using the same setup as in Part A, turn the aperture to one of the mid-sized openings. Move the screen toward and away from the screen. When is the image in focus? Is the image only in focus at a fixed location, or is there a range over which the image appears to be in focus? Over what distance can you move the screen while keeping the image in focus?

In photography, there is a term known as the depth of field. This refers to the range over which an image appears to be in focus. For example, in a photo with a large depth of field, you might see a person in the foreground with scenery in the background, and all of these subjects are in sharp focus. A narrow depth of field yields a single object in focus, while the scenery and background are out of focus. This is sometimes used to draw the viewer’s attention to an object.

2.	Predict: Look at the different openings on the aperture apparatus in your setup. Do you think the larger or smaller apertures will produce greater depths of field? Justify your answer.

4.	 Set the aperture to the largest setting. Beginning with the screen far away from the lens, move the screen closer until the image produced first appears to be in good focus. Record the distance.

5.	Continue moving the screen toward the lens until the image just begins to lose focus. Record this second distance.

6.	Find the difference between the two distances to calculate the range of focus. Record this value in the Data Table.

7.	Repeat Steps 4 - 6 with each of the round apertures, with 5 being the largest, and 1 being the smallest. Which aperture has the greatest depth of field?

data table

| Aperture | Depth of field |
| --- | --- |
|  | (cm) |
| 5 (largest) |  |
| 4 |  |
| 3 |  |
| 2 |  |
| 1 (smallest) |  |

| Color | Color | Drops |
| --- | --- | --- |
| Prediction | Reality |  |

# Text boxes

Station 1

Station 3

Describe image here

Describe image here

Station 2

Station 4